## Slide 1: Flow control instructions
Jump instruction:
Syntax is
JMP destination_label
Start : mov ah,2 ;display a character
mov dl,’L’
int 21h
jmp start

## Slide 2: Range of a Conditional jump
The jump instruction requires that destination_label must proceed the jump instruction by no more than 126 bytes

## Slide 3: How the CPU implements a conditional jumps
(1) signed jump
JG/JNLE jump if greater than
ZF=0 and SF=OF
JGE/JNL jump if greater than or equal to
jump if not less than equal to
SF=OF

## Slide 4
Unsigned Conditional jumps
JA/JNBE jump if above if CF=0 and ZF=0
JB/JNAE jump if below if CF=1
jump if not above
or equal

## Slide 5
3) single-flag jumps
JE/JZ jump if equal if ZF=1
jump if equal to 0
JC jump if carry if CF=1

## Slide 6: The CMP instruction
The jump instruction is often provided by the CMP (compare) instruction
CMP destination,source
Eg:
CMP AX,BX
JZ TOP

## Slide 7: Larger of Two numbers
The following code compares the unsigned values in AX and BX and moves the larger of the two to DX
mov dx,ax ;assume AX is integer
cmp ax,bx ; if AX is >=BX then
jae loop ; jump to loop if above or equal
mov dx,bx ;else move BX to DX
Loop: mov ax,4c00h
int 21h

## Slide 8: High level language structure
IF –THEN
IF condition is true
THEN
execute true-branch statements
END-IF

## Slide 9: Simple if statement
If (a=b) then
<statement1>
<statement2>
End if
Assembly language code
Cmp ax,bx
Je true
Jmp endif
True:
<statement1>
<statement2>
End if

## Slide 10: Compound if statement
If (al>op1)
or (al>=op2
or(al=op2)
or(al<op4) then
<statement1>
End if

## Slide 11
cmp al,op1 ;if al>op1 then
jg L1 ;jump to L1
cmp al,op2 ;else if al>=op2 then
jge L1 ; jump to L1
cmp al,op3 ; else if al=op3 then
je L1 ; jump to L1
cmp al,op4 ; else if al<op4 then
jl L1 ;jump to L1
jmp L2 ;else jump to L2
L1: <statement> ;L1:execute <statement>
L2 : ;end if

## Slide 12: For loop
FOR 80 times DO
display ‘*’
END_FOR
The code is
MOV CX,80 ; number of stars to display
MOV AH,2 ;display character function
MOV DL,’*’ ;character to display
TOP:
INT 21h ;display a star
LOOP TOP ;repeat 80 times