## Slide 1: The processor status and the Flags register
The status flags are located in bits 0,2,4,6,7 and 11
The control flags are located in bits 8,9 and 10

## Slide 2
Flag names and symbols
Status flags
Bit name symbol
0 carry flag CF
2 Parity flag PF
4 Auxiliary carry flag AF
6 Zero flag ZF
7 Sign flag SF
11 Overflow OF

## Slide 3
Control flags
Bit Name symbol
8 Trap flag TF
9 Interupt flag IF
10 Direction flag DF

## Slide 4: The status flag
The processor uses the status flags to reflect the result of an operation.
For eg : SUB AX,BX is executed, the zero flag becomes 1, there by indicating that a zero result was produced.

## Slide 5: Carry flag
CF =1 if there is a carry out from the most significant bit(msb) on addition, or there is a borrow into the msb on subtraction; otherwise, it is 0,
CF is also affected by shift and rotate instructions

## Slide 6: Parity flag
PF=1 if the low byte of a result has an even number of one bits(even parity). It is 0 if the low byte has odd parity.
Eg: if the result of a word addition is FFFEh, then the low byte contains 7 one bits, so PF=0

## Slide 7: Auxiliary carry flag(AF)
AF = 1 if there is a carry out from bit 3 on addition, or a borrow into bit 3 on subtraction. AF is used in binary coded(BCD) operations

## Slide 8: Zero flag
ZF = 1 for a zero result, and ZF =0 for a nonzero result

## Slide 9: Sign flag
SF = 1 if the msb of a result is 1; it means the result is negative if you are giving a signed interpretation. SF=0 if the msb is 0

## Slide 10: Overflow flag
OF = 1 if signed overflow occurred, otherwise it is 0.

## Slide 11: How the instructions are affect the flags
Instruction affects flags
Mov/xchg none
Add/sub all
Inc/dec all except CF
Neg all

## Slide 12
Example
ADD AX,BX where AX contains FFFFh, and BX contains FFFFh
Soln:
FFFFh
FFFFh
---------
1 FFFE

## Slide 13
The result stored in AX is
FFFEh = 1111 1111 1111 1110
SF=1 because msb is 1